## Slide 1
Essential training
for introduction of
HepB-BD vaccine
Module 4
Hepatitis B vaccine characteristics and storage
ver. 11/24
Notes: This module corresponds to Chapter 5 and Annex 1 of ‘A guide for Introducing and Strengthening Hepatitis B birth dose vaccination’: Vaccine products and logistics

## Slide 2: Learning objectives
At the end of the module you will be able to:
  Describe characteristics of the HepB vaccine
  Describe vaccine storage requirements
  Take steps to handle suspected frozen vaccines
  Estimate vaccine needs
Duration: 30 minutes

## Slide 3
Characteristics and presentation of the vaccine
Formulas for forecasting vaccine supply needs
Key messages
What to do in case suspected of frozen vaccine
Vaccine storage requirements
Learning content

## Slide 4: Characteristics and presentation of the vaccine
Only a monovalent vaccine can be used for HepB vaccination at birth
The monovalent HepB is presented as a liquid in 1, 2, 6, 10 and 20-dose vials
The country will use X-dose vial from X-manufacturer*
Notes: NOTE1 : add a photo of the vaccine vial that is provided by your immunization programme
NOTE 2: EDIT BULLET 3 to specify the vial size and manufacturer of vaccine that will be used in your country

## Slide 5: The checks of vaccine quality
Before administering vaccine, do these checks to make sure you are giving potent vaccine:
Vaccine stored in correct temperature? Check temp logs
Vaccine got too hot? Make sure VVM has not reached the discard point
Vaccine got too cold? If freezing suspected, do shake test
Vaccine is too old? Check the expiry date
Vaccine vial is already open? Check that all multi-dose vial policy (MDVP) criteria are met*
Notes: Remember this slide from previous module?
Lets go into a little more detail and specifically discuss VVM, prevention of freezing & testing for freezing (and MDVP, if applicable).

## Slide 6: How to check VVM status?
Before administering the vaccine, you need to check the Vaccine Vial Monitor (VVM) on the vaccine vial

## Slide 7: Why watch out for freezing? HepB vaccine is extremely freeze-sensitive
HepB is relatively heat-stable…
…but highly sensitive to freezing!
Notes: This figure shows the vaccine heat and freeze sensitivity.
As you can see, HepB-BD is highly freeze-sensitive but relatively heat-stable.

## Slide 8
Where should the HepB vaccine be stored in the refrigerator?
Notes: NOTE:
HepB-BD vaccine should not be placed in or near the freezer portion of the refrigerator nor directly on a frozen ice pack.
Keep the HepB-BD vaccine away from all cold air vents
8

## Slide 9: Cool boxes and vaccine carriers
Handling the cool boxes and vaccine carriers:
Condition the ice packs: Shake until you can hear water moving inside
Place them in the vaccine carrier along with an electronic freeze indicator (Freeze Tag). No freeze tag is needed if using cool water packs.
Do not put HepB vaccine in direct contact with ice packs
Put the foam pad on top and carefully close the lid.
Notes: If vaccine transport is required, only conditioned ice packs or cool water packs should be used to maintain a cold chain at +2°C to +8°C
Frozen ice packs should be kept at room temperature for 30 or more minutes until the ice inside begins to melt. This is called “conditioning” the ice packs and prevents the vaccine from freezing when it is placed near the packs
It is most important NOT to put HepB vaccine directly on the ice packs
If using conditioned ice packs for transporting HepB vaccine, a freeze indicator should also be placed in the cool box or carrier. No freeze indicator is needed if using cool water packs.

## Slide 10: What to do in case of suspected frozen vaccine
If freezing is suspected, the shake test should be conducted, particularly if the following conditions are observed:
Low temperature alarm on the continuous temperature recorder
Refrigerator temperature below 0⁰C
Vaccine vial in contact with frozen ice packs
Cross (X) on the Freeze Tag
If the shake test shows that freezing has occurred, remove all vaccines from the same batch, note the quantity concerned, and discard all affected vaccines.
Complete and submit appropriate forms to indicate vaccines and supplies loss.

## Slide 11: How to conduct a shake test (1/2)

## Slide 12: How to conduct a shake test (2/2)

## Slide 13: Examples of shake test vial results
Nearly transparent
Thick sediment
Notes: Sedimentation rate in the non-frozen vial is very slow.
On the left, this slide shows a vial of vaccine that has been frozen → thick sediment rapidly forms at the bottom.
On the right, you see a non-frozen vial → you see a cloudly liqued because sediments float and do not rapidly sink to the bottom. This means the vaccine has not been frozen and is safe to use.

## Slide 14: Multi-dose vial policy (MDVP)
HepB monovalent vaccine may be kept and used for up to 4 weeks (28 days) if all of the following multi-dose vial policy conditions are met:
→ Vaccine has VVM on the body of the vial (not the cap)
→ Expiry date has not passed
→ VVM has not reached the discard point
→ Caps have not been submerged in water
→ Aseptic techniques have been used to withdraw all doses (no obvious signs of contamination)
Notes: NOTE: Use this slide only if your country has a multi-dose vial policy
WHO policy on the use of opened multi-dose vaccine vials (2014 Revision)
https://www.who.int/publications/i/item/WHO-IVB-14.07

## Slide 15: How to forecast HepB vaccine supply needs for a catchment area
Target population: for HepB-BD this should be “Number of Live Births per year”
Coverage target: example, “90% coverage”
Number of doses in schedule: example, “1” if only use for BD
Wastage factor: example, “1.1” for 1-dose vial (10% wastage)
Answer: for example, if target is 100 newborns, the number of doses needed is 100 x .90 x 1 x 1.1 = 99 doses
x
A.
Target
Population
for year
x
B.
Coverage
target
C. Number of doses
in schedule
x
D.
Wastage
factor
E.
Answer:
Number of doses
needed for year
=

## Slide 16: Key messages
Vaccine used for HepB-BD is monovalent, liquid, and will contain X-doses in each vial.
The estimate of vaccine and supplies needed is calculated using a method based on the target population.
The vaccine must be refrigerated between +2⁰C and +8⁰C, and must never be frozen. If freezing is suspected, the SHAKE TEST should be conducted.
If country uses multi-dose vial policy, all criteria of this policy must be followed before using an open vial of vaccine*
Notes: NOTE 1: Edit bullet 1 according to vaccine used in your country
NOTE2: Keep bullet 4 if applicable

## Slide 17: End of the module
Thank you for your attention

## Slide 18: References
WHO: A Guide for Introducing and Strengthening Hepatitis B Birth Dose Vaccination http://apps.who.int/iris/bitstream/10665/208278/1/9789241509831_eng.pdf
WHO. Practices to improve coverage of the hepatitis B birth dose vaccine. https://www.who.int/publications/i/item/practices-to-improve-coverage-of-the-hepatitis-b-birth-dose-vaccine
WHO policy on the use of opened multi-dose vaccine vials (2014 Revision) https://www.who.int/publications/i/item/WHO-IVB-14.07